## Slide 1
Hotel Network Design
with Guest and Administration VLANs
NETWORK OVERVIEW
Router0 Cisco 1941
Switch0 Cisco 2960
PC0 Guest
PC1 Guest
PC2 Admin
PC3 Admin
STUDENT NAMES: Bhagyashree Patel • Fancy Patel • Mahek Pithiya • Krina Chothani
FACULTY:MS.Pragya Vats DEPARTMENT: UIT
Focus: VLAN segmentation, router-on-a-stick, and ACL-based access control

## Slide 2
Introduction and Problem Statement
2
THE PROBLEM
• Guests use the network for personal devices. • Hotel administration uses computers for internal work. • Guest and administration traffic should be separated. • Unrestricted access can create security risks.
OUR SOLUTION
• Create Guest VLAN 10 and Administration VLAN 20. • Use separate IP subnets and router gateways. • Configure an 802.1Q trunk between switch and router. • Apply the extended ACL GUEST_FILTER to block Guest-to-Admin traffic.
VLAN 10 · GUEST | VLAN 20 · ADMIN | ACL · GUEST_FILTER

## Slide 3
Project Objectives
3
01
Design a small hotel network in Cisco Packet Tracer
02
Create Guest VLAN 10 and Administration VLAN 20
03
Assign static IP addresses to four PCs
04
Configure router subinterfaces and an 802.1Q trunk
05
Apply an extended ACL to restrict Guest-to-Admin traffic
06
Test connectivity and verify the ACL behavior
Goal: same-VLAN communication succeeds; Guest-to-Administration traffic is blocked.

## Slide 4
Network Topology
4
Router0 Cisco 1941
Switch0 Cisco 2960
Fa0/24 trunk · VLANs 10, 20
PC0 192.168.10.10 VLAN 10 · Guest
PC1 192.168.10.11 VLAN 10 · Guest
PC2 192.168.20.10 VLAN 20 · Admin
PC3 192.168.20.11 VLAN 20 · Admin
DEVICES
• 1 Cisco 1941 router • 1 Cisco 2960 switch • 4 PCs
PORT MAPPING
• Fa0/1–Fa0/2 → VLAN 10 • Fa0/9–Fa0/10 → VLAN 20 • Fa0/24 → trunk

## Slide 5
VLAN and IP Address Configuration
5
VLAN 10 · GUEST
Network: 192.168.10.0/24 Gateway: 192.168.10.1
VLAN 20 · ADMINISTRATION
Network: 192.168.20.0/24 Gateway: 192.168.20.1
PC | IP Address | Subnet Mask | Default Gateway | VLAN
PC0 | 192.168.10.10 | 255.255.255.0 | 192.168.10.1 | 10
PC1 | 192.168.10.11 | 255.255.255.0 | 192.168.10.1 | 10
PC2 | 192.168.20.10 | 255.255.255.0 | 192.168.20.1 | 20
PC3 | 192.168.20.11 | 255.255.255.0 | 192.168.20.1 | 20
A VLAN creates a separate logical network. The default gateway lets a PC send traffic to other networks.

## Slide 6
Implementation and Security Configuration
6
SWITCH CONFIGURATION
• VLAN 10 named GUEST • VLAN 20 named ADMIN • Fa0/1–Fa0/2 assigned to VLAN 10 • Fa0/9–Fa0/10 assigned to VLAN 20 • Fa0/24 configured as 802.1Q trunk • Allowed VLANs: 10, 20
ROUTER SUBINTERFACES + ACL
interface g0/0.10 encapsulation dot1Q 10 ip address 192.168.10.1 255.255.255.0 ! interface g0/0.20 encapsulation dot1Q 20 ip address 192.168.20.1 255.255.255.0 ! ip access-list extended GUEST_FILTER deny ip 192.168.10.0 0.0.0.255 192.168.20.0 0.0.0.255 permit ip any any ! interface g0/0.10 ip access-group GUEST_FILTER in
ACL placement: inbound on Router0 GigabitEthernet0/0.10 (Guest VLAN subinterface)

## Slide 7
Testing and Results
7
Test | From → To | Command | Expected / observed result
1 | PC0 → PC1 | ping 192.168.10.11 | Successful
2 | PC2 → PC3 | ping 192.168.20.11 | Successful
3 | PC0 → Guest gateway | ping 192.168.10.1 | Successful
4 | PC2 → Admin gateway | ping 192.168.20.1 | Successful
5 | PC0 → PC2 | ping 192.168.20.10 | Blocked by GUEST_FILTER
WHAT SUCCESS SHOWS
Devices communicate within their own VLANs and reach their gateways.
SECURITY RESULT
Guest-to-Administration ping fails, consistent with the ACL.

## Slide 8
Conclusion and Future Scope
8
CONCLUSION
• Designed and simulated the hotel network in Packet Tracer. • Created separate Guest and Administration VLANs. • Configured static IPs, router gateways, and trunking. • Applied GUEST_FILTER to restrict Guest-to-Admin traffic. • Verified expected connectivity using ping tests.
FUTURE SCOPE
• Add DHCP for automatic IP addressing. • Add a wireless access point for guest Wi-Fi. • Configure NAT and internet connectivity. • Add policies for more hotel departments. • Add network monitoring and logging.
THANKYOU